## Slide 1: Accelerators and detectors
Máté Csanád (Eötvös U)

## Slide 2: Contents
Accelerators in general
Details of SPS, RHIC, LHC
Detectors in general
Some examples: PHENIX, STAR, CMS, NA61

## Slide 3: Electrostatic particle accelerators
Basic electrostatic
Cockroft-Walton
Van de Graaf
Limitation: length and/or insulation breakdown

## Slide 4: Linear accelerators
Alternating current to always accelerate towards the next tube
Multiple types: Wideroe, Alvarez, Tesla, RFQ

## Slide 5: Cyclotrons
Circular design, larger acceleration possible
Spiral: increasing radius as particle energy increases
Beam exiting towards target

## Slide 6: Synchrontrons
Basic principle: maintain constant radius
Synchronize magnetic field to particle energy
Three tasks:
  Accelerating
  Bending
  Focusing

## Slide 7: Relativistic kinematics
Lorentz-multiplication of four-vectors: ,
  Metric tensor:
Space-time four-vectors:
  Length: proper-time, Lorentz-scalar,
Momentum four-vector: ,
  Velocity: ; Rest energy: ; Lorentz-factor:
  Full energy: , (let us use from here)
Lorentz-boost: multiplication with , in the direction of
  , ; similarly for space-time
Scalar: invariant under Lorentz-boost (, yes; : no)

## Slide 8: Kinetic energy
Classical: ; relativistic:
Series expansion:

## Slide 9: Particle accelerators
Fwd acceleration: electric field,
Circular orbit: magnetic field,
  Radius: ;
  1 eT = 0.3 (GeV/c)/m 1 T field, 0.3 GeV/c particle, 1 m radius
Cyclotron: acceleration between semicircles
Synchrotron: fixed orbit
cyclotron

## Slide 10: Buckets and Bunches
Acceleration with RF cavities
Particles must always see an accelerating voltage
Storage ring (”accelerator”): buckets
Bunch: where the voltage is accelerating in the bucket
Synchronous particle (A)
Others: oscillate (B) sometimes late, sometimes early

## Slide 11: Bunch crossings and collisions
Two rings with opposite directed beams
Crossing at some angle
  Crab cavity: rotation
Bunch spacing: determined by pre-accelerators
Not all bunches are filled: filling scheme
Bunch crossing: possible collisions
  Missing bunches: pre-accelerator and injection kicker gap
  Important: abort gap for dumping the beam
Max number of events usually too high
Filtering: minimum bias sampling

## Slide 12: Contents
Accelerators in general
Details of SPS, RHIC, LHC
Detectors in general
Some examples: PHENIX, STAR, CMS, NA61

## Slide 13: Facilities: Large Hadron Collider (+SPS)
LHC collisions: p+p, p+Pb and Pb+Pb; also Xe+Xe, soon probably O+O
Energies: from 2.76 TeV/nucleon to 13 TeV (p+p only)
Experiments: ALICE, ATLAS, CMS, LHCb, LHCf, MoEDAL, TOTEM
Phase diagram related studies: SPS (NA61/SHINE, previously NA49)
Energy: ; usually quoted: (E per nucl. pairs)

## Slide 14: CERN, LHC and SUrroundings
Mont Blanc
Geneve
Lake Geneva
Swiss-French border
CERN

## Slide 15: LHC in Numbers
2x27 km, 150-200 m deep
Collisions: 4 intersections
~3000 bunches, 25 ns spacing
99.9999991% speed of light
10 000 rounds/sec
600 million collisions/sec
10 000 superconducting magnets
10 000 tons of liquid N2: 80 K
120 tons of liquid He: 2 K
120 MW electricity consumption (c.f. a large city)
6 mg H+ in 10 years
25 000 terabyte data yearly

## Slide 16: The Relativistic Heavy Ion Collider
At the Brookhaven National Laboratory, Long Island, New York, USA
Collisions of , d, 3He, Al, Cu, Zr, Ru, Au, U (each has separate reason)
Accelerator energies: 7.7-200 GeV/nucleon, even 0.51 TeV for
Experiments: STAR, sPHENIX; past: BRAHMS & PHOBOS & PHENIX

## Slide 17: Areal Photo of RHIC

## Slide 18: RHIC in Numbers
Two rings, 4 km each
99.995% speed of light
111 bunches
80 000 rounds/sec
Thousands of collisions/sec
1740 superconducting magnets
21 000 km superconducting wires
25 tons of liquid He
0.00005 mg gold/year

## Slide 19: Rhic runs, 2001-2022

## Slide 20: STAR Recorded data

## Slide 21: Future facilities: NICA, FAIR, J-PARC HI
New facilities planned/built
NICA: 2020, MPD&BM@N
FAIR: 2022, CBM
J-PARC HI: 2025, JHITS
FAIR phase 1
FAIR phase 2
SIS100/300
NICA
J-PARC HI

## Slide 22: (FUTURE) FacilitIES comparison
Many future facilities and experiments, SPS and RHIC already running
RHIC, NICA: Collider and fixed target
SPS, FAIR, J-PARC: fixed target
Energy ranges from 2 to 20 GeV in
Compilation from Daniel Cebra and Olga Evkidomiv:
Facility | RHIC BES-II & Fixed Target | SPS | NICA | FAIR | J-PARC HI
Experiment | STAR | NA61 | MPD & BM@N | CBM | JHITS
Start | 2019 | 2009 | 2020-23 | 2025 | 2025
Energy (, GeV) | 2.9-19.6 GeV | 4.9-17.3 | 2.0-11 | 2.7-8.2 | 2.0-6.2
Rate | 100-1000 Hz | 100 Hz | 10 kHz | 10 MHz | 10-100 MHz
Physics | Critical Point Onset of Deconf. | Critical Point Onset of Deconf. | Onset of Deconfinement Compr. Hadronic Matter | Onset of Deconfinement Compr. Hadronic Matter | Onset of Deconfinement Compr. Hadronic Matter
Facility | RHIC BES-II & Fixed Target | SPS | NICA | FAIR | J-PARC HI
Experiment | STAR | NA61 | MPD & BM@N | CBM | JHITS
Start | 2019 | 2009 | 2020-23 | 2025 | 2025
 | 2.9-19.6 GeV | 4.9-17.3 | 2.0-11 | 2.7-8.2 | 2.0-6.2
Rate | 100-1000 Hz | 100 Hz | 10 kHz | 10 MHz | 10-100 MHz
Physics | Critical Point Onset of Deconf. | Critical Point Onset of Deconf. | Onset of Deconfinement Compr. Hadronic Matter | Onset of Deconfinement Compr. Hadronic Matter | Onset of Deconfinement Compr. Hadronic Matter

## Slide 23: Contents
Accelerators in general
Details of SPS, RHIC, LHC
Detectors in general
Some examples: PHENIX, STAR, CMS, NA61

## Slide 24: Particle detectors
Bubble chamber: overheated fluid, bubble creation
Cloud chamber: supersaturated gas, condensation
Ionization detector: traversing particle ionizes gas
Scintillator: luminescence, light detection
Semiconductor detectors: similar to CCD chip
Many Nobel prizes: Wilson, Glaser, Charpak

## Slide 25: Event characterisation objectives
When (time zero) and where (vertex)
Overlap (centrality), number of participants (Npart)
Orientation with respect to overlap (reaction plane)
Central Au+Au
Npart~300
Peripheral Au+Au
Npart~50
d+Au
p+p
Reaction Plane
Reality

## Slide 26: Time zero & vertex determination
BBC at , charged particles
  Event activity
ZDC at , evaporating neutrons
  Spectator size
Time zero from
Vertex from
North
South
L
L
TN
TS
Vertex position: (TS-TN)  c/2
Time zero: (TN+TS)/2 – L/c

## Slide 27: Collisions of different centrality
Centrality: how head-on the collision was
Measure: how many events are more central?
  0%: most central collision; 0-5%: most central 1/20th of all; 90-100%: least central 1/10th of all
Central
INTRODUCTION EXPERIMENTS OBSERVATIONS
Peripheral

## Slide 28: Centrality determination
Participants: new particles towards central detectors, including BBC
Spectators: deflected by DX magnet
  Evaporated neutrons: not deflected („zero degree”), towards ZDC
Spectators
Participants
Towards ZDC
Central detectors, incl. BBC
Spectators

## Slide 29: Centrality calibration
More central: more charge in BBC
Very central or very peripheral: no energy in ZDC
EZDC versus QBBC
Simulation via Glauber Monte Carlo model
Simulation
Data
0-5%
5-10%
10-15%

## Slide 30: Glauber model
Nuclear density: , : radius, : thickness,
, surface density profile, with
, nuclear overlap function
, number of binary collisions
, total cross section
, initial excentricity
Monte Carlo: deposit nucleons according to , collision probability, etc.

## Slide 31: Results from a Glauber MC Calculation
GeV Au+Au simulation in varios centrality classes

## Slide 32: Results from a Glauber MC Calculation
GeV Au+Au simulation in varios centrality classes
Npart vs. b
Ncoll vs. b
Prob(Ncoll=100) vs. b
TAB vs. b

## Slide 33: Reaction plane determination
Segmented detector, charge in the -th segment
b
impact parameter
Reaction plane
BBC
RxNP
Reaction Plane

## Slide 34: Particle properties
Particle = spatial track
  Set of hits in several detectors measured
Momentum measured via curvature
  Known magnetic field
Particle type determined via mass & charge
  Charge: curvature again…
  Mass: momentum & (velocity or energy)
Measure all this for hadrons, g, leptons etc…
Quality assurance: matching of the above

## Slide 35: Magnetic field to measure momentum
Momentum from curvature, precise tracking needed
CMS

## Slide 36: Tracking with Kalman Filter
5D state vector: , measurement vector:
Describing the helical track of the particle
Adding more measurement points from detector layers
ATLAS
ALICE
CMS

## Slide 37: Particle Identification via Time of flight
Time of Flight → velocity → mass → particle identity

## Slide 38: Particle id via energy deposition
Deposited energy: Bethe-Bloch formula
  Depends on mass and medium
Example plot from STAR:

## Slide 39: Electron ID: Cerenkov detectors
Čerenkov radiation: , angle
Example in PHENIX: Ring Imaginc CHerenkov counter (RICH)
Čerenkov light mirrored onto PMT plane
PMT array, ring size characteristic

## Slide 40: Data Aquisition (DAQ)
Central concept: triggering
Level-1: hardware trigger
Level-2: software trigger
All connected to global timing
Event building at the end

## Slide 41: Event Builder
Event fragments come in from all detectors
Need to be assembled
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
SEB
SEB
SEB
SEB
SEB
SEB
SEB
SEB
SEB
SEB
Gigabit
Switch
Buffer
Box
Buffer
Box
Buffer
Box
Buffer
Box
Sub-event buffers
Assembly & Trigger Processors
Final Storage
One event

## Slide 42: Contents
Accelerators in general
Details of SPS, RHIC, LHC
Detectors in general
Some examples: PHENIX, STAR, CMS, NA61

## Slide 43: An example: the PHENIX Detector system
Charged hadrons (pion, kaon, etc.)
Photons, direct or decay (from , )
Light mesons , and
Single leptons → heavy flavor
Dileptons → heavy flavor, J/Ψ

## Slide 44: Tracking in PHENIX
Track particles, measure momentum
  Hit → Track → Curvature → Momentum
Wire chambers
Track reco: DC+PC1
Matching: PC2-3

## Slide 45: Tracking in PHENIX, illustrated
Innermost layers, tracking
Outer layers: matching, reduces background, for example decays

## Slide 46: Time of flight PID in PHENIX
Time Of Flight detector
  time measurement
  120 ps resolution
East and West arm
  1472 PMTs
Measure hit position and time from PMT time
PMT
PMT

## Slide 47: Lepton and Photon ID: EM Calorimeters
Energy + momentum → mass
Leptons and photons to deposit all their energy in EMCal
Lead Scintillator and Lead Glass: light ~ energy
Hadron ID via time of flight: additional recalibration needed (worse time resol.)
Pb absorber
generates shower
Scintillator
generates light
Optical fiber
collects light
PMT
PbSc
PMT
Scintillator
generates Č-rad
PbGl

## Slide 48: further example: Silicon detectors @ CMS

## Slide 49: Time projection chamber @ STAR
Heart of STAR: a large Time Projection Chamber for tracking and ID

## Slide 50: A fixed-target detector system: NA61
TPCs for tracking and PID, TOF for more precise PID, PSD for centrality

## Slide 51: What do we extract from the data?
px, py, pz → h or y, j, pt or mt
Transverse mom. spectrum for each particle
Rapidity distributions
Angular distributions
  Elliptic flow
All kinds of ratios
Pair-correlations
  Momentum, angle, etc
Fluctuations
Whatever tells us something…

## Slide 52: BACKUP